## Slide 1: Chapter 4
Gates and Circuits

## Slide 2: Chapter Goals (1 of 2)
Identify the basic gates and describe the behavior of each
Describe how gates are implemented using transistors
Combine basic gates into circuits
Describe the behavior of a gate or circuit using Boolean expressions, truth tables, and logic diagrams

## Slide 3: Chapter Goals (2 of 2)
Compare and contrast a half adder and a full adder
Describe how a multiplexer works
Explain how an S-R latch operates
Describe the characteristics of the four generations of integrated circuits

## Slide 4: Computers and Electricity (1 of 2)
Gate
A device that performs a basic operation on
electrical signals
Circuits
Gates combined to perform more
complicated tasks

## Slide 5: Computers and Electricity (2 of 2)
How do we describe the behavior of gates and circuits?
Boolean Expressions
Uses Boolean algebra, a mathematical notation for expressing two-valued logic
Logic Diagrams
A graphical representation of a circuit; each gate has its
own symbol
Truth Tables
A table showing all possible input values and the associated
output values

## Slide 6: Gates
Six types of gates:
  NOT
  AND
  OR
  XOR
  NAND
  NOR
Typically, logic diagrams are black and white with gates distinguished only by their shape
We use color for clarity (and fun)

## Slide 7: NOT Gate
A NOT gate accepts one input signal (0 or 1) and returns the complementary (opposite) signal as output
Representations of a NOT gate

## Slide 8: AND Gate
An AND gate accepts two input signals
If both are 1, the output is 1; otherwise,
the output is 0
Representations of an AND gate

## Slide 9: OR Gate
An OR gate accepts two input signals
If both are 0, the output is 0; otherwise,
the output is 1
Representations of an OR gate

## Slide 10: XOR Gate (1 of 2)
An XOR gate accepts two input signals
If both are the same, the output is 0; otherwise,
the output is 1
Representations of an XOR gate

## Slide 11: XOR Gate (2 of 2)
Note the difference between the XOR gate and the OR gate; they differ only in one input situation
When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0
XOR is called the exclusive OR because its output is 1 if (and only if):
Either one input or the other is 1
Excluding the case that they both are

## Slide 12: NAND Gate
The NAND (“NOT of AND”) gate accepts two input signals
If both are 1, the output is 0; otherwise,
the output is 1
Representations of a NAND gate

## Slide 13: NOR Gate
The NOR (“NOT of OR”) gate accepts two inputs
If both are 0, the output is 1; otherwise,
the output is 0
Representations of a NOR gate

## Slide 14: Gates with More Inputs
Some gates can be generalized to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1
Representations of a three-input AND gate

## Slide 15: Constructing Gates (1 of 3)
Transistor
A device that acts either as a wire that conducts electricity or as a resistor that blocks the flow of electricity, depending on the voltage level of an input signal
A transistor has no moving parts, yet acts like a switch
It is made of a semiconductor material, which is neither a particularly good conductor of electricity nor a particularly good insulator

## Slide 16: Constructing Gates (2 of 3)
Note: If an electrical signal is grounded, it is “pulled low” to zero volts
A transistor has three terminals:
  A collector (or source)
  A base
  An emitter
What’s the output in Figure 4.8?
  If the base signal is low, the transistor acts like an open switch, so the output is the same as the source
  If the base signal is high, the transistor acts like a closed switch, so the output is pulled low
What gate did we just describe?
The connections of a transistor

## Slide 17: Constructing Gates (3 of 3)
The easiest gates to create are the NOT, NAND, and NOR gates
Constructing gates using transistors

## Slide 18: Circuits
Combinational Circuit
The input values explicitly determine the output
Sequential Circuit
The output is a function of the input values and the existing state of the circuit
We describe the circuit operations using:
  Boolean expressions
  Logic diagrams
  Truth tables

## Slide 19: Combinational Circuits (1 of 4)
Gates are combined into circuits by using the output of one gate as the input for another
This same circuit using a Boolean expression is AB + AC

## Slide 20: Combinational Circuits (2 of 4)
Three inputs require eight rows to describe all possible input combinations

## Slide 21: Combinational Circuits (3 of 4)
Consider the following Boolean expression A(B + C)
Does this truth table look familiar?
Compare it with the previous table.

## Slide 22: Combinational Circuits (4 of 4)
Circuit Equivalence
Two circuits that produce the same output for identical input
Boolean Algebra
Allows us to apply provable mathematical principles to help design circuits
A(B + C) = AB + BC (distributive law) so circuits must be equivalent

## Slide 23: Properties of Boolean Algebra

## Slide 24: Adders (1 of 4)
At the digital logic level, addition is performed in binary
Addition operations are carried out by special circuits called, appropriately, adders

## Slide 25: Adders (2 of 4)
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10 in base two
Half Adder
A circuit that computes the sum of two bits and produces the correct carry bit
Truth table

## Slide 26: Adders (3 of 4)
Circuit diagram representing a half adder
Boolean expressions
sum = A  B
carry = AB

## Slide 27: Adders (4 of 4)
Full Adder
A circuit that takes the carry-in value into account
A full adder

## Slide 28: Multiplexers (1 of 2)
Multiplexer (or MUX)
A circuit that uses a few input control signals to determine which of several input data signals is routed to its output signal

## Slide 29: Multiplexers (2 of 2)
The control lines S0, S1, and S2 determine which of eight other input lines (D0…D7) are routed to the output (F)
A block diagram of a multiplexer with three select control lines

## Slide 30: Circuits as Memory (1 of 3)
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

## Slide 31: Circuits as Memory (2 of 3)
An S-R latch stores a single binary digit (1 or 0)
There are several ways an S-R latch circuit can be designed using various kinds of gates
An S-R latch

## Slide 32: Circuits as Memory (3 of 3)
Assume that S and R are never both 0 at the same time
The design of this circuit guarantees that the two outputs X and Y are always complements of each other
The value of X at any point in time is considered to be the current state of the circuit
Therefore, if X is 1, the circuit is storing a 1; if X is 0, the circuit is storing a 0
An S-R latch

## Slide 33: Integrated Circuits (1 of 3)
Integrated Circuit (also called a chip)
A piece of silicon on which multiple gates have been embedded
Silicon pieces are mounted on a plastic or ceramic package with pins along the edges that can be soldered onto circuit boards or inserted into appropriate sockets

## Slide 34: Integrated Circuits (2 of 3)
Historically, integrated circuits have been classified by the number of gates (or transistors) they contain
As of 2014, chips exist with over 20 billion transistors

## Slide 35: Integrated Circuits (3 of 3)
An SSI chip containing independent NAND gates

## Slide 36: CPU Chips
The most important integrated circuit in any computer is the central processing unit, or CPU
Each CPU chip has a large number of pins through which essentially all communication in a computer system occurs

## Slide 37: Ethical Issues
Codes of Ethics
Which professional organization is more focused on the hardware side?
Which is more focused on the software side?
How are their codes of ethics alike?
How do they differ?

## Slide 38: Who Am I?
I didn’t get much recognition at the time, but my book formed the basis for the development of digital computers. Can you name its contribution?

## Slide 39: Do You Know?
What is the name of the study of materials
smaller than 100 nanometers?
What topic in computer science education is referred to as “the tenth strand”? Who wrote about the fundamental problem of expressing thought by means of symbols?
What did Maurice Wilkes realize in 1949?
What two (or more) concepts can be referred to by the term “computer ethics”?